## Slide 1
MODELING INSTITUTIONAL RISK AND THE COST OF NUCLEAR POWER
645 – Computational Economics
December 16, 2025
Tyler Linnebur
1

## Slide 2
01
06
02
03
07
04
05
Research Question & Motivation
If I had a Magic Wand
Methods
Methods
Conclusion
Data Sources/ Assumptions
Difficulties & Results
What This Presentation Covers
2

## Slide 3
Research Question & Motivation
3
How do permitting regimes and ownership structures affect nuclear power costs once construction duration and schedule risk are explicitly priced into financing?
Why this matters:
  Nuclear is essential for firm, low-carbon electricity and deep decarbonization
  Yet new nuclear is widely viewed as uneconomic based on standard Levelized Cost of Energy (LCOE) comparisons
  Empirical evidence shows construction duration dominates cost outcomes
  Long and uncertain timelines sharply increase financing costs
  Standard LCOE models treat construction time as fixed and ignore risk pricing

## Slide 4
Methods - Model Components
4
Sets / Indices
  Ownership type: private, public
  Permitting regime: baseline, reform → Defines the four institutional cases being compared
Parameters
  Engineering and cost inputs (held constant):
    Capital cost, O&M cost, fuel cost (from OECD-NEA)
  Financing inputs:
    Base WACC by ownership
    Construction duration by permitting regime
    Schedule risk (dispersion of construction time)
  Risk pricing parameter:
    Converts schedule uncertainty into higher financing cost
Variables
  x(o,r): weight placed on each ownership–permitting case
  Z: selected levelized cost of electricity (LCOE)
Objective Function
  Minimize total LCOE across cases
  Optimization selects the lowest-cost ownership–permitting combination
Constraints
  Weights across cases must sum to one
  All weights must be nonnegative → Forces selection of exactly one institutional configuration
Notes: - x(o,r) is a switch that turns on the cheapest case. Part of the linear program
- Z is the objective value of the model. represents the chosen levelized cost of electricity, in dollars per megawatt-hour, after the model selects the lowest-cost case.

## Slide 5
Methods - Cost Formation & Selection
5
Interest during construction (IDC):
  Capital is tied up for years before revenue begins
  Longer builds and higher discount rates compound financing costs
  Midpoint compounding approximates spending over construction
Cost minimization:
  Only capital costs adjust for construction risk
  O&M and fuel costs held constant
  Optimization selects the lowest-cost ownership–permitting combination
  No behavioral assumptions, just transparent comparison
Selects the minimum LCOE across ownership and permitting cases
Objective Function
Selection Constraints
Forces the model to choose exactly one ownership–permitting configuration
Effective discount rate (risk pricing):
  Base WACC differs by ownership
  Schedule risk, measured as dispersion in construction time, raises required returns
  Investors price uncertainty ex ante, not just realized delays
  κ is a calibration parameter

## Slide 6
Data Sources/ Assumptions
6
Reactor-level construction data from the International Atomic Energy Agency, Power Reactor Information System (IAEA PRIS)
  Construction start to commercial operation
  Cancelled and incomplete units excluded
  Compared 10 plants for baseline and reform groups
Two empirical cohorts:
  Baseline permitting:
    Long average build times - 14.92 years
    Very high dispersion - 10.36 years
  Reformed permitting:
    Shorter builds - 6.44 years
    Low dispersion - 0.66 years
Cost inputs:
  OECD-NEA LCOE tables (capital, O&M, fuel)
  Plant Type: LWR (1100 MW)
Financing assumptions obtained from OECD NEC literature:
  Private WACC ≈ 8%
  Public WACC ≈ 2.5%

## Slide 7
Difficulties & Results
7
Formulation Difficulties
  Nuclear projects are rare and heterogeneous
  Construction delays are institutional, not random
  Investors price risk, not just expected duration
  Need a tractable proxy for schedule uncertainty
  Tradeoff between realism and transparency
  Deterministic structure chosen to make mechanisms obvious
Results
  Permitting reform has a first-order effect on LCOE
  Reduction in schedule risk matters more than average build time
  Financing effects dominate all other cost components
  Ownership matters, but conditionally:
    Public ownership lowers costs only when permitting is predictable
    Under baseline permitting, high risk overwhelms financing advantages
  Lowest-cost case:
    Public ownership + reformed permitting (~$76/MWh)
  Highest-cost case:
    Private ownership + baseline permitting

## Slide 8
If I had a Magic Wand
8
If I Had Unlimited Time, Money, Energy
  Move from deterministic to stochastic construction timelines
  Model full cash flows during construction and operation
  Endogenize investment timing and option value
  Compare regulatory regimes across countries explicitly
  Model RAB, CWIP, loan guarantees, and risk-sharing instruments
  Embed this framework into a power system expansion model

## Slide 9
Conclusion
9
  Nuclear cost problems are fundamentally institutional risk problems
  Regulatory predictability matters more than speed alone
  Ownership structure is secondary to permitting coherence
  Standard LCOE comparisons overstate inherent nuclear cost
  Policy debates focusing only on technology or subsidies miss the main drive

## Slide 10
THANK YOU
10

## Slide 11
Refereces
  Bowen, M., Evans, A., Khan, H., & Ponangi, R. T. (2024). Reforming nuclear reactor permitting and environmental reviews: Roundtable report. Columbia University, Center on Global Energy Policy. https://www.energypolicy.columbia.edu
  Foster, J., Wagner, L., & Bratanova, A. (2014). LCOE models: A comparison of the theoretical frameworks and key assumptions (No. 4-2014). School of Economics, University of Queensland, Australia.
  Grubler, A. (2010). The costs of the French nuclear scale-up: A case of negative learning by doing. Energy Policy, 38(9), 5174–5188.
  Guaita, N., Spangler, R. M., & Hansen, J. (2025). Parametric and nonparametric models of U.S. cost overruns for nuclear power plants (INL/CON-25-84516-Revision-0). Idaho National Laboratory. https://www.inl.gov
  International Atomic Energy Agency. (n.d.). PRIS Country Details: China. Power Reactor Information System. https://pris.iaea.org/PRIS/CountryStatistics/CountryDetails.aspx?current=CN
  International Atomic Energy Agency. (n.d.). PRIS Country Details: Republic of Korea. Power Reactor Information System. https://pris.iaea.org/PRIS/CountryStatistics/CountryDetails.aspx?current=KR
  International Atomic Energy Agency. (n.d.). PRIS Country Details: United States of America. Power Reactor Information System. https://pris.iaea.org/PRIS/CountryStatistics/CountryDetails.aspx?current=US
  Jacobs, J., Jantarasami, L., & Fishman, X. (2024, January). Licensing and permitting reforms to accelerate nuclear energy deployment. Bipartisan Policy Center.
  Lovering, J., Yip, A., & Nordhaus, T. (2016). Historical construction costs of global nuclear reactors. Energy Policy.
  Lovering, J. R., Nordhaus, T., & Yip, A. (2017). Apples and oranges: Comparing nuclear construction costs across nations, time periods, and technologies. Energy Policy, 102, 650–654.
  Nuclear Innovation Alliance. (2024). Key recommendations for reforming U.S. nuclear energy regulation. Washington, DC: Nuclear Innovation Alliance.
  OECD-NEA. (2021). Unlocking reductions in the construction costs of nuclear: A practical guide for stakeholders (NEA No. 7530). OECD Publishing.
  OECD-NEA. (n.d.). Levelised cost of electricity calculator. https://www.oecd-nea.org/lcoe/
  OECD-NEA. (2022). Financing new nuclear power plants: Minimising the cost of capital by optimising risk management (NEA No. 7632). OECD Publishing. https://www.oecd-nea.org
  Portugal-Pereira, J., Ferreira, P., Cunha, J., Szkló, A., Schaeffer, R., & Araújo, M. (2018). Better late than never, but never late is better: Risk assessment of nuclear power construction projects. Energy Policy, 120, 158–166.
  U.S. Energy Information Administration. (n.d.). How much electricity in the United States is generated from nuclear? U.S. Department of Energy. https://www.eia.gov/tools/faqs/faq.php?id=228&t=3
  U.S. Energy Information Administration. (2022, November 18). Nuclear explained: Data and statistics. U.S. Department of Energy. https://www.eia.gov/energyexplained/nuclear/data-and-statistics.php